##### IMPLEMENTATION OF REGULATORY FRAMEWORK

TASK IDENTIFICATION FORM

Date Originated:  2000-05-02

Date Revised:      2005-05-18

WORKING GROUP:	Network

TASK #:	5	File:	NTTF005Z

TASK TITLE:	Impact of "roaming"’ on intercarrier interfaces

TASK DESCRIPTION: 	To the extent that operational, interworking, or parametric issues may exist with the advent of technologies which manifest aspects of Terminal Mobility, this task will identify, confirm, and resolve issues associated with the advent of technologies which facilitate Terminal Mobility also commonly referred to as "roaming".

For the purpose of this TIF, Terminal Mobility is defined as the ability of a terminal to access telecommunication services from different locations and while in motion, and the capability of the network to identify and locate that terminal.

PRIORITY: 1		Critical Task:	 N	DUE DATE:	   Q4/05

CROSS IMPACTS:		Any TIF pertaining to intercarrier interconnection interfaces

WORK PLAN AND TIME FRAMES:

For the purpose of this TIF, discussions will initially be based on the postulation that calls destined to a roaming terminal will be exchanged between carriers in the 'home exchange' associated with the mobile terminal.  The home exchange may be derived by the Central Office code of the subscriber's telephone number consistent with the one NPA-NXX per exchange rule prescribed in Decision 97-8 and reaffirmed in Telecom Order 97-1572.  For calls which are originated by the roaming terminal, the calls will nominally be routed towards the destination exchange in accordance with network interconnection rules without necessarily having to route the call back to the home exchange.

The NTWG will address potential issues according to the following process:

- Members of the NTWG will identify potential issues.  Members which identify potential issues will define the scope and/or nature of the operational/parametric/internetworking issue and describe the situation the issue may arise as well as provide an analysis of the impact associated with the issue;

- The members of the NTWG will confirm the validity of the issue;

- The members of the NTWG will seek a resolution to the issue and augment and/or modify the affected specifications and/or guidelines (including other consensus documentation) accordingly (it is also possible that new specification(s) may be required);

- Solutions that are the object of a consensus by the NTWG will be documented accordingly and presented to the Steering Committee for approval;

- Where consensus cannot be reached, a status report will be submitted to the Steering Committee by the NTWG.

CURRENT STATUS: 	Open

TASK ORIGINATORS:

Simon-Pierre Olivier

Director - Regulatory Affairs

Fido Solutions Inc.

800 de La Gauchetière Street W, Suite 4000

Montreal, Quebec

Fido™:  	(514) 994-0211

Office:	  	(514) 937-0102, ext. 8319

Fax:	  	(514) 572-1833

E-Mail: 	simon-pierre.olivier@fidomobile.ca

TASK TEAM:	Members of Network Working Group

ACTIVITY DIARY:

| Serial | Date | Activity |
| --- | --- | --- |
| 1 to 62 | From 00-02-08 to 01-10-02 | Meeting Minutes / Discussions from 2000-Feb-08 to 2001-Oct-02. See NTTF005X on the CRTC CISC Web Site |
| 63 | 01-10-31 | PN 2001-110 was issued by the Commission on October 31, 2001. |
| 64 | 03-09-09 | Commission rendered Telecom Decision 2003-53 on August 12, 2003. All parties agreed to close NTTIF005. |
| 65 | 2005-04-18 | Contribution NTCO303 was filed by Bell Canada. This contribution discusses wireless equal access and contains information on how to populate the JIP parameter in the SS7 IAM message. NTWG members agreed to re-open TIF5. [Note from the TIF Owner: Because the last version of TIF5 is 44 pages long (version NTTF005X), serials #1 to 62 were deleted by the TIF Owner. The TIF Owner suggests that NTTF005X must remain accessible on the CRTC CISC Web site.] |
| 66 | 05-04-18 | Bell presented NTCO303, entitled “Wireless CLEC Equal Access”, dated March 2005. In the contribution, Bell wrote that: “The purpose of this contribution is to inform the industry that the standards for populating JIP to indicate originating location information are now available”. Bell provided an excerpt from an NIIF document, which contains 7 rules for populating the JIP. Keith Richardson noted that in Rule #3 the NIIF does not recommend proposing that the JIP parameter be mandatory. Fido clarified that the JIP is to be used by the IXCs solely for the purpose of offering “distance sensitive billing plan”. Fido added that one of its vendors already confirmed that the JIP can not be populated with cell-site information. As specified in the NIIF document, the JIP could be populated with an NPA-NXX that is assigned in the LERG to the originating MSC. However, this is not desirable when the originating MSC serves multiples exchanges. Fido will validate this information with its other vendors. Fido also recommended that IXCs should validate whether their billing systems would be able to read and interpret the JIP. Fido also committed to provide the group with a letter that was sent by the Telecommunications Industry Association (TIA) to the NIIF, in November 2003, which list multiple technical reasons as to why the JIP can not be populated with cell-site information. The group agreed to add an addendum to NTRE008. Bell agreed to be the author for this addendum. |
| 67 | 05-05-17 | NTTF005Y was reviewed. NTWG participants did not have any comment on TIF notes (serials #65 & 66). In response to a question that was asked by Bell, Fido confirmed that it still intends to file a contribution on this subject before the July 19 conference call. The NTWG Chairman confirmed that the group should target Q4/2005 for submitting the new report / addendum to the Commission. |

ACTION REGISTER:

| Action | Opened | Prime | P - Date | A – Date | Status |
| --- | --- | --- | --- | --- | --- |
| 1 | Provide contributions on roaming issues | 00-02-08 | All |  |  | Closed |
| 2 | Provide 2nd Version of TIF | 00-05-02 | Bohdan Z. | 00-06-03 | 00-05-05 | Closed |
| 3 | Provide 3rd (accepted) Version of TIF | 00-06-12 | Bohdan Z. | 00-07-18 | 00-06-12 | Closed |
| 4 | Confirm OLI values used by U.S. wireless carriers for originating Equal Access calls. | 00-06-12 | Bohdan Z. | 00-07-18 | 00-07-18 | Closed |
| 5 | Draft an addendum to NTRE008 | 05-04-18 | ALL |  |  | Open |

ASSOCIATED CONTRIBUTIONS:

| Date | Contributor | Title | File name on CRTC Web page |
| --- | --- | --- | --- |
| 00-02-08 | Telus Communications Inc. | Roaming Issues - Wireless & IP | NTCO072.doc |
| 00-03-07 | Bell Canada | VoIP - IXC Traffic | NTCO077.doc |
| 00-03-07 | Telus Communications Inc. | Roaming Issues - Wireless & IP | NTCO079.doc |
| 00-05-02 | Telus Communications Inc. | Geographic Number Portability Definition | NTCO083.doc |
| 00-05-02 | Telus Communications Inc. | Additional Roaming Issues to the March 7,2000 List | NTCO084.doc |
| 00-05-02 | Bell Canada | Roaming Issue – Call Origination | NTCO085.doc |
| 00-05-02 | Clearnet Communications Inc. | Roaming Issues – Cordless Phones | NTCO087.doc |
| 00-06-12 | AT&T Canada, Call-Net, Videotron Telecom Inc. | Roaming Issues | NTCO088.doc |
| 00-06-12 | Keith Richardson | Comments on the scope of NTF00X | NTCO089.doc |
| 00-06-12 | Clearnet Communications Inc. | Roaming Issues - the U.S. Environment | NTCO090.doc |
| 00-06-12 | Telus Communications Inc. | TELUS Response to resolution of roaming issues proposed in NTCO87 | NTCO091.doc |
| 00-07-18 | Telus Communications Inc. | Examples supporting issues identified in contributions NTCO079A and NTCO84 | NTCO092.doc |
| 00-07-18 | Clearnet Communications Inc. | Forwarded proposed version of TIA/EIA 93-B - Wireless Telecommunications Ai-Di Interfaces Standard | NTCO087.doc |
| 00-10-11 | Bell Canada | Scope of work and Term of Reference | NTCO106.doc |
| 00-10-11 | Microcell | Equal Access in a Wireless World | NTCO107.doc |
| 00-10-11 | Bell Canada | Wireless CLEC Roaming | NTCO108.doc |
| 00-10-11 | Telus Communications Inc. | Wireless CLEC Roaming Issues | NTCO109.doc |
| 00-10-11 | AT&T Canada | Wireless CLEC Roaming Issues | NTCO110.doc |
| 00-10-27 | Bell Canada | Distance Insensitive Billing Scheme | NTCO111.doc |
| 00-10-27 | TELUS | Wireless CLEC Roaming Issues | NTCO112.doc |
| 00-10-27 | Microcell | Equal Access within the Digital Coverage | NTCO113.doc |
| 00-10-27 | TELUS/Bell Canada | Report on Billing and Routing Alternatives Associated with Roaming Subscribers of Wireless CLECs | NTCO114a (and following versions "b" and "c") |
| 00-11-14 | Microcell | Equal Access on Mobile Terminating Calls | NTCO115 |
| 00-11-14 | Vidéotron Limitée | IXC Screening on Roaming Calls | NTCO116 |
| 00-11-14 | Bell Canada | Wireless CLEC Roaming - Billing Options | NTCO117 |
| 00-11-14 | Bell Canada | Wireless CLEC - Toll-free Access | NTCO118 |
| 00-11-14 | TELUS | Wireless CLEC Roaming Issues | NTCO119 |
| 00-12-08 | NTWG | Report on Billing & Routing Alternatives | NTRE008 |
| 01-02-07 | Microcell | Scope of Wireless Equal Access | NTCO120 |
| 01-02-27 | Bell Canada | Equal Access on Mobile Terminating Calls | NTCO124 |
| 01-03-20 | Bell Canada | Draft Report on MTC in Equal Access Environment | NTCO126a (and following versions "b" and "c") |
| 01-05-01 | NTWG | Report: Equal Access on Mobile Wireless Terminating Calls | NTRE009 |
| 01-05-29 | Bell Canada | Roaming Updates | NTCO132 |
| 01-10-31 | CRTC | PN 2001-110 was issued by the Commission | n/a |
| 03-08-12 | CRTC | Commission rendered Telecom Decision 2003-53 | n/a |
| 05-04-18 | Bell Canada | Wireless CLEC Equal Access | NTCO303 |

Table 1 - Potential terminal mobility issues related to CISC specifications and consensus documents

|  | Item | Description | Priority | Comments |
| --- | --- | --- | --- | --- |
|  | 911 Address Validity | Whether scenarios exist where a roaming customer would place a 9-1-1 call and his/her home address would be displayed at the receiving PSAP, and if so, how to deal with these scenarios. |  |  |
|  | Originating IX Call Routing and Trunk Forecasting | How originating IX calls (other than 8XX) should be routed from a roaming-capable CLEC to an IXC, and how the required trunk groups can be reliably forecasted. |  |  |
|  | Terminating IX Call Routing | How terminating IX calls should be routed when a subscriber is roaming away from his/her home location. |  |  |
|  | IX Call Blocking | How to ensure that valid IX calls are not blocked in a roaming equal access environment. |  |  |
|  | IX Call Billing | How to facilitate accurate billing of IX calls (other than 8XX) in a roaming equal access environment. |  |  |
|  | 8XX Call Routing and Trunk Forecasting | How 8XX calls should be routed from a roaming-capable CLEC to an ILEC, and how the required trunk groups can be reliably forecasted. |  |  |
|  | 8XX Call Billing and Service Availability | How to facilitate accurate billing and service availability for 8XX calls. |  |  |

# Footnotes

Planned completion date.

Actual completion date.